## Slide 1: AMIE: Affine-Attentive Matching and Interpretive Imprint Evaluation for Partial Fingerprint Verification
Tsai-Chieh Chen*, Ching-Te Chiu* Ned Lin†, Ang Yu†, Paul Lai†, Daniel Chen† Chia-Yi Lin*
* Department of Computer Science, National Tsing Hua University, Taiwan † FocalTech Electronics Co., Ltd., Taiwan

## Slide 2: Outline
Introduction
Detector: High-Coverage Keypoint Extraction
Matcher: Affine-Attentive Keypoint Matching
Verifier: Final Decision on Aligned ROI Pair
Experimental Results
Conclusion

## Slide 3: Introduction - Background
Mobile devices now use smaller sensors, capturing only partial fingerprints.
Traditional minutiae-based matchers fail on partial prints due to
  Few detectable minutiae and poor overlap.
  Distortions from pressure, dry/wet skin, and image degradation.
  Accuracy drops sharply when ridge detail is poor.
Fig. 1. Examples of challenging partial fingerprint pairs (top) and overlap showcases (bottom)
Small overlap area + poor quality
Wet fingers causing ridge swelling
Blurry prints with slight distortion from pressure or angle

## Slide 4: Introduction - Contributions
Having robustness by detecting keypoints in almost every ridge block.
  SuperPoint-based Detector with stride-4 and fingerprint-specific fine-tuning.
Aligning pairs reliably under minimal overlap.
  Geometry-aware attention via 24-param RPE (Relative Positional Encoding) in LightGlue
  Combined with MAGSAC++ for affine fitting at low overlaps
Interpretable, CNN-free, avoids heuristic segmentation/cropping .
  Affine-warped binary mask defines pixel-accurate ROI (Region of Interest, possible overlapped area).
Generalizing across different sensors without re-training.
  Lightweight ResNet (1.28M parameters) classifies only the aligned, ROI-masked region

## Slide 5: Introduction - Data flowchart
Detector
  A SuperPoint-based keypoint detector for high-coverage fingerprint features.
Matcher
  An affine-attentive matcher combining LightGlue with FC-GNN and followed by affine alignment via MAGSAC++ for geometry-aware attention.
  A pixel-level, affine-warped binary ROI mask enabling interpretable imprint localization.
Verifier
  An ROI-aware verifier based on a lightweight ResNet, operating exclusively on aligned and masked regions.
Fig. 2. Pseudo algorithm of AMIE
Fig. 3. Overview of AMIE modules and data flow

## Slide 6: Detector: High-Coverage Keypoint Extraction
Role
Predict keypoints and descriptors for input images
Inputs: Image pair
Outputs: Keypoints and Descriptors Where is the number of top response by NMS is the descriptor dimension

## Slide 7: Matcher: Affine-Attentive Keypoint Matching
Role
Match keypoints and descriptors
Inputs: Keypoints and Descriptors
Outputs: Similarity matrix
Fig. 5. Matcher module architecture

## Slide 8: Verifier: Final Decision on Aligned ROI Pair
Role
Final decision head that takes the aligned, imprint-masked ROI pair and predicts a single match probability
Inputs: Concatenated ROI-masked imprints
Outputs: Scalar probability , indicating “same finger”

## Slide 9: Experiment – Dataset & Settings
We evaluate models on three datasets
  NASIC (primary), MixDataset (composed) and FT9399 (vendor-held)
Training on i9-12900K with one RTX 3090 Ti
Compared with JIPNet, PFVNet, DeepPrint and AFR-Net
All of models are trained on NASIC, and harmonized to accept 17630 inputs
EER, FRR@FAR=0.01% and MCE are used as the metrics
Table 1. Information of each dataset

## Slide 10: Experiment – Result
AMIE is over six times more compact than any other baselines
AMIE provides state-of-the-art accuracy, efficiency, and robustness across both challenging real and synthetic benchmarks.
Table 2. Performance of each model on different dataset

## Slide 11: Conclusion
AMIE
  A geometry-aware pipeline for partial fingerprint verification
  Combines DetectorMatcherVerifier with explicit alignment + ROI masking
  Achieves robust and interpretable verification by enforcing geometry aware alignment and co-visible region masking
Performance Achievements
  NASIC: EER ↓ 2.26%, FRR₀.₀₁% ↓ 6.07% (state-of-the-art)
  MixDataset: Alignment (MCE ↓ 6.24 px) while keeping EER < 1%
  Outperforms JIPNet, PFVNet, DeepPrint, AFRNet across strict operating points
  Only 6.2M params, inference 6.8 ms/pair (vs. 38–57M params for baselines)
Insufficiency
  Alignment accuracy may degrade in cases of extremely minimal overlap or rotation degree exceeds