## Slide 1: Tenstorrent Progress Report 9/1 林家逸

## Slide 2: Outline
Experiment – serialized vs. batched

## Slide 3
warmup = 2, iterations = 30, tiles-per-core = 8
serialized
  send Q, K, V from DRAM to L1 MEM one by one
batched
  send Q, K, V from DRAM to L1 MEM simultaneously
serialized vs. batched

## Slide 4
Result
 | Denominator | serialized | batched
iteration exec time |  | ~ 54.3 us | ~ 54.8us
compute input wait | SELF_ATTENTION | ~ 8.9% | ~ 9.4%
Reader CB backpressure | READER | 20.7% | 42.4%
Writer wait for compute | WRITER | 86.6% | 87.4%
Output CB wait | SELF_ATTENTION | ~ 0.38% | ~ 0.38%
batched need more time to wait input and read input from DRAM to L1 MEM, since when Q and K is sent, compute kernel can start calculation